# Title: Fermentative biohydrogen production in a novel biodisc bioreactor: Principle and Improvement.

# Laurent Beckers*, Serge Hiligsmann, Julien Masset, Christopher Hamilton, Philippe Thonart

# PhD, Member of CWBI (Walloon Center of Industrial Biology), University of Liège, Belgium

E-mail: lbeckers@ulg.ac.be

# Abstract

1. Biohydrogen investigation at CWBI Hydrogen is widely considered as the most promising energetic carrier. At an industrial scale, steam-reforming of methane is currently the major hydrogen-producing process. H2 may also be produced from renewable resource such as carbohydrates wastes from agriculture or agro-food industries. This technology is based on anaerobic fermentation, called dark fermentation, by chemotrophic bacteria. The fermentative production of hydrogen from renewable biomass could at least partially reduce our dependence on fossil fuel, produce “green” energy and decrease the carbon dioxide emissions. It offers the potential production of usable hydrogen from a variety of renewable resources.

The investigations carried out at CWBI involve selection and characterization of bacteria strains able to produce biohydrogen efficiently and from a wide range of substrates. The selected strains at the laboratory has been characterised as Clostridium sp.

2.  Enhancement of hydrogen production in a biodisc bioreactor In order to produce hydrogen at high yields and production rates, the biotechnological process needs to be further optimized and efficient bioreactors must be designed. A biodisc bioreactor has been design and investigated to produce biohydrogen from glucose by the Clostridium butyricum CWBI1009 strain at a high yield and production rate. This reactor, working continuously, has an internal volume of 2.3l but a working volume (liquid phase) of 300ml. Firstly, it enhances the hydrogen production rate (by about 3 times more than a completely stirred bioreactor) by partially fixing the bacteria on the porous support and thus increasing the cell concentration in the bioreactor (decoupling of HRT and SRT). Secondly, the rotating biodisc design enables efficient gas transfer (hydrogen and carbon dioxyde) from the liquid phase where it is produced by the bacteria to the headspace. Indeed, this is an important way to increase hydrogen production yields (by about 25% compared to a completely stirred bioreactor) by allowing the bacteria to focus on the metabolites pathways that produce more hydrogen. Other reactors designs have shown such good results by increasing the interfacial surface.

Our work concludes the importance of providing efficient liquid to gas transfer in the biohydrogen-producing reactors to enhance the hydrogen production and reach higher yields and production rates. Such an approach may open the way for efficient scaled up hydrogen production bioreactors and processes.

# Biography

Laurent Beckers, chemistry engineer, is master in engineering sciences from the University of Liège (ULg) in 2008.  He began PhD researches on biohydrogen production at the Walloon Center of Industrial Biology (CWBI) in October 2008 with a grant of the FNRS, National Funds for Scientific Research. The thesis focuses on a new approach of the hydrogen mass transfer problem. A goal of the thesis is to develop a model linking the biohydrogen production performances and the transfer efficiency in novel prototypes bioreactors developed in the center.

The work presented is part of a project ARC 07/12-04 called MicroH2 granted by the CFB (French Community of belgium). More information is available at www.microh2.ulg.ac.be.