Structural model of the mitral valve

included in a cardiovascular closed loop model

- S. Paeme1, K. Moorhead1, JG. Chase2, CE. Hann2, B. Lambermont1, P. Kolh1,

- M. Moonen1, P. Lancellotti1, P.C. Dauby1, T. Desaive1

- 1 Cardiovascular Research Center, University of Liège, Liège, Belgium

- 2 Department of Mechanical Engineering, University of Canterbury, Christchurch, New Zealand

#### Abstract

This research describes the integration of a structural model of the mitral valve in an existing closed-loop cardiovascular system (CVS) model.

Keyword(s): modeling of physiological systems

#### Introduction

A minimal cardiovascular system (CVS) model including mitral valve dynamics has been previously validated in silico [1]. However valvular parameters of this model are difficult to link with structural and anatomical components of the valve.

#### Models and methods

This research uses a simple dynamic model of the stiffness of the valve leaflets to characterize their fundamental effects on flow and pressure. The valve is described as a non-linear rotational spring or a ‘hinge’ with the angle change under pressure driven flow being related to the stiffness and the damping of the valve:

where c is the damping coefficient, θ is the valvular leaflet opening angle, the FK(θ) is the non-linear restoring force,  is the transmitral pressure, and α is a torque constant converting differential pressure into an input torque on the valve.

This model is included in a CVS model consisting of 7 elastic chambers [1].

#### Results

Figure 1 shows the evolution of mitral valve area during one cardiac cycle. The maximum mitral valve values reached during the E-wave and A-wave as well as timing of these two periods correspond to the physiological data [2,3]. Figure 2 shows the evolution of transmitral blood flow during one cardiac cycle with the E-wave amplitude nearly 10 times bigger than the A-wave amplitude as expected physiologically [3].

Fig. 1: Mitral valve area evolution during one cardiac cycle

Fig. 2: Transmitral flow evolution during one cardiac cycle

#### Conclusions

This study shows that this valvular model included in a CVS closed loop model gives physiological results.

##### This proof-of-concept study demonstrates that this generic structural valve model could be used to investigate the hemodynamic repercussions of several pathological conditions, such as mitral regurgitation or stenosis.

##### References

- Paeme, S. et al. Mathematical multi-scale model of the cardiovascular system including mitral valve dynamics. Application to ischemic mitral insufficiency. Biomed Eng Online, 10, 86, 2011

- Saito, S. et al. Mitral valve motion assessed by high-speed video camera in isolated swine heart. Eur J Cardiothorac Surg, 30, 584-91, 2006

- Flewitt, J.A. et al. Wave intensity analysis of left ventricular filling: application of windkessel theory. Am J Physiol Heart Circ Physiol, 292,6, 2817-23, 2007