# Feasibility study of the modernization of Wielingen class frigates

J. Marchal Professor – University of Liège

A. Hage Associate Professor – University of Liège

C. Dessart Research Engineer – University of Liège

J. Matagne Research Engineer – University of Liège

# Abstract: The research group MRN04 has made a study of modernization of frigates of the Belgian Navy. The modernization includes fitting out of a landing area for an 11 tonnes helicopter, modifying the superstructure to solve the problems of cracks and reducing the radar cross section.

The proposal of the group MRN04 consists of widening and stiffness the stern deck in order to permit landing of a helicopter, surrounding the existing superstructure by a new envelop having a better furtivity.

The resistance of the helicopter landing area and the rigidity of the superstructure has been estimated by structural computations by finite elements method, which permits to choose the most adequate structure.

Once the weight of the new elements is known, a new estimation of the weight is established. It permits to calculate the draft and the trim, and serves as the data to calculate the ship resistance. In fact, the speed of the frigate, as a crucial point, should not decrease too much. The ship resistance will be obtained by means of model tests in the towing tank in the University of Liège.

The study shows the possibility to lay out a landing area for a helicopter of 11 tonnes as well as to decrease significantly the radar cross section, without severe reduction of the frigate speed.

Acknowledgements:

The Belgian ministry of defence is financing since 2002 a research programme MRN-04 at the University of Liège.¶ The aim of this research is to create an expertise and to develop calculation modules to help the Navy in their decision for the acquisition of materials.

# Introduction

This study concerns of modernization of the Wielingen class frigates of the Belgian navy.

Following the request of the Belgian navy, the feasibility study includes:

- The reduction of the RCS (Radar Cross Section) of the ship by modifying the external geometry, principally at the super structure.

- Laying out a helicopter landing area

- Solving the problem of cracks initiation in the superstructure.

The proposed solution to reduce the RCS of the ship consists of inclining their external vertical side, limiting to theirs maximum the surfaces and the openings. The proposed configuration has been verified afterwards by another research group, which has measured the RCS (Radar Cross Section) at scale model.

Concerning the helicopter landing area, the resistance of the initial stern structure of the ship was insufficient to support the landing of a NH90 helicopter. A local strengthening has therefore been proposed.

The calculations of the structural resistance of the landing area and that of the strengthening to avoid cracks spread in the superstructure have been realized by using finite elements method, the complete structure of the frigate has previously been modelled in order to do the calculation.

These modifications have significantly changed the weight and the position of the gravity centre of the ship. The studies on stability, seakeeping and ship resistance have been made.

In fact, the modifications should not be accompanied by the reduction of the seakeeping performance or of the ship speed.¶ The studies on hydrodynamics performances have experimentally been realized in the towing tank of the University of Liège.

The studies of modernization are realized in such ways:

- Proposition of a new design

- Calculation of the structural resistance of the landing area

- resolution of the problem of cracks in the superstructure

- new estimation of the weight.

- experimental ship résistance tests

- experimental seakeeping tests

# New design proposal

The present superstructure of the frigate is formed from numerous vertical sides with several openings; this configuration offers a very bad RCS.

It is the same for the non-immerged part of the hull, which has a surface with a vertical side.

The figure 1 represents the actual form of the frigate.

Model of the actual frigate

The reduction of the RCS consists of inclining the vertical sides and reducing to the maximum the exposed area.

The construction of such a new superstructure will be too expensive. Therefore the solution consists of enveloping the present superstructure by a metallic hull having a good RCS. This envelop will have the side inclining for about 8° with regard to the vertical, and the area of the exposed surface will be minimal. This envelop does not play any role in structural resistance, at least its contribution to the resistance is worthless to be taken into consideration.

As far as the landing area of the helicopter is concerned, the ship stern breadth proves to be too narrow to permit landing of a helicopter of 11 tonnes. In fact, the minimal breadth of the landing area should be 12.2m. So it is necessary to widen the landing deck.

The proposed solution is to widen the stern deck by 2 m, the hull structure will be fitted at the new deck and will have a more inclined side, with the aim of decreasing the RCS.

The figure 2 represents the new configuration.

Model of the modified frigate

The views of face of the forms are shown in figure 3. It permits to well visualize the inclined side of the new configuration.

Present (left) and new (right) configuration

# Calculation of the structural resistance of the helicopter landing area

The structural resistance of the landing area has been calculated by using the finite element method. Static linear computation have been done and dynamic effects were taken into account by a load coefficients

The figure 4 shows a part of the global model used to execute the calculation by the finite element method.

Numerical model of the frigate

The calculation shows that the initial structure is not strengthen enough to permit the landing of a helicopter of 11 tonnes. Local modifications have been proposed, for both the thickness and the frames of the deck. The deck thickness is increased to 14mm and the number of reinforced stiffeners at the critical places is doubled.

VM stress in initial structure

VM stress in the modified structure

It results in a decrease of the maximal Von-Mises stress from 110 N/mm² (linear calculation) to 180 N/mm² (see the figures 5 and 6).

The study gives rise to an increase of weight of only 3.5 tonnes. This weight is obtained after a comparison of different reinforcements.

# Resolution of the problem of cracks in the superstructure

The cracks appear at some opening of the superstructure, and they spread from the corners of the openings due to the concentration of stress.

Those cracks are dangerous to cause tears leading to increase the damage of the superstructure, it is necessary to reinforce local structure in order to prevent their spread and to have a sufficient resistant structure. In addition, the frigate is supposed to be under the protections against the attacks NBC, the presence of cracks is unacceptable.

A crack observed in the superstructure is shown in the figure 7.

Fissure at the opening of the superstructure

As in the previous study, the cause of the cracks has been investigated by using numerical software. The figure 8 shows the part of the numerical model used in the calculations.

View of the numerical model used for simulation

The structural calculation has revealed that the cracks appear due to the shape of the opening. Severe concentrations of stress can be observed very often at the corner of the opening, especially for the shape corner. When a classification society rule bending moment is applied, the stress at certain places exceeds the admissible standard. In fact the linear elastic calculation has revealed that the Von Mises stress exceeds 300N/mm² in the aluminium plates.

VM stress in the initial structure

VM stress in the new structure.

# The error of conception has been corrected by applying circle corner and adding some transversal bars to rigidify the openings.

# The figures 9 and 10 represent the results obtained for initial structure and for modified structure.

# New estimation of weight

For the resistance and seakeeping tests in towing tank (see figure 11), it is necessary to estimate the weight of the ship, the longitudinal position of the gravity centre, as well as the inertias around it. After all the proposed modifications are made, a detailed estimation of the weight has been made.¶

The estimation of weight shows that the weight of ship in ballast condition passes from 1880 tonnes to 2065 tonnes.

It corresponds to an increase of the weight of 9.8% with regard to the initial configuration.

# Ship resistance test

The tests of ship resistance were carried out with 1/40 scale model in the towing tank of the University of Liege.

The purpose is to compare the curves of ship resistance in two configurations: initial and modified.

The tests correspond to a range of ship speed from 8 to 28 knots. The tests were realised in three different load conditions.

  - Loaded to 10%

  - Loaded to 75%

  - Full loaded

During the model tests, the ship resistance, the draft and the trim are measured and registered.

Model on the scale of 1/40.

Figure 12 curve of ship resistance

The evolution of the resistance in three different loading cases is given in the figure 12. Not much variation of ship resistance is observed while comparing the two resistance curves of the ships (initial and modified configurations).

A reduction of the frigate speed will be expected on the order of 1 knot, when the propulsion characteristics are unchanged.

# Seakeeping tests

The tests of seakeeping (see figure 13), carried out in the same towing tank, are aiming at verifying that the seakeeping performance of the frigate does not deteriorate by the proposed modifications.

Besides the same position of the gravity centre for model and real ship, the similitude rules for the inertias of rotation around the two axes (X and Y) of the ship have to be respected in order to extrapolate to the full scale.

During the seakeeping tests, the ship model was free in the towing tank.

Figure 13 Test of seakeeping

Three angles of incidence and two types of the wave spectrums (J.O.N.S.W.AP and Pierson-Moskowitz) are selected. The Pierson-Moskowitz spectrum is given in figure 14.

The angles of incidence of 0°, 45° and 90° are fixed in advance.

Figure 14	Pierson-Moskowitz spectrum

A camera records the movements of the ship model. This camera picks up the movement of LEDs fixed to the upper part of the model. The movements of yawing, rolling and pitching are measured.

Figure 15	Pitching, rolling and yawing movement. Pierson-Moskowitz spectrum at Hs = 8 cm. no incidence.

An example of the curves obtained during a test of seakeeping is given in the figure 15, where the blue curve represents the temporal evolution of the wave, the green is for the movement of yawing, the red is that of rolling, and the black the rotation of pitching. The results demonstrate that after modifications, the ship keeps good seakeeping performance.

# Conclusions

A study of feasibility study of modernization of the Wielingen class frigates has been realized. The modernization concerns the laying out of a helicopter landing area, the reducing of the RCS of the ship, and the resolution of the problem of cracks in the superstructure.

The study relates to several domains: design, hydrodynamics, structure and it requires different tools: numeric simulations, model tests in towing tank…

The proposed modification, consisting of enveloping the existing superstructure by a hull with inclined sides and widening the deck at stern of the ship, constitutes a viable solution.

In fact, these modifications reduce significantly the RCS of the ship, allow the landing of a helicopter of 11 tonnes, all of these have a slight influence over the hydrodynamic behaviours of ship (seakeeping and ship resistance), the reduction of the maximal speed will be around 1 knot.

# Text boxes

Von-mises stress (BV):74N/mm²